## Slide 1: Webinar: Establishing Predicted Environmental Concentrations for API Loss from Pharmaceutical Manufacturing
PSCI PiE/AMR Topic Team
Arcadis
14 October 2021

## Slide 2: Speakers
Nolan Chase
EIT, Consultant and PiE Specialist
Arcadis
Jason Rushing
PE, Principal Engineer and PiE Subject Matter Expert
Arcadis
Elizabeth C. Girardi-Schoen
Global Environmental Sustainability Leader
Pfizer

## Slide 3: Special Thanks
Special thanks to the members of the PSCI team who developed this detailed guidance:
Ann Lee-Jeffs (Teva)
Elizabeth Girardi-Schoen (Pfizer)
Jeffrey Brenchley (Merck)
Jonathan Stanway (GSK)
Neil Parke (Eli Lilly)
Todd Davidson (Bristol Myers Squibb)
Vincent Parker (Elanco)
And to the members of external consultancy Arcadis:
Jason Rushing
David Riedel
Nolan Chase

## Slide 4: Introduction
Pharmaceuticals in the Environment (PiE) is an increasing public concern.
While manufacturing losses represent a small percentage of API entering the environment, the pharmaceutical industry and PSCI have committed to addressing the risk of API losses from manufacturing.
Many companies are requiring that their facilities, and their suppliers, estimate mass losses from manufacturing to determine the predicted environmental concentration (PEC).
The industry-accepted method for estimating API mass loss is to follow a mass balance approach, where inputs, outputs, and losses are accounted for to determine the mass entering wastewater.
PSCI has developed a set of detailed guidance documents on how to perform a PiE mass balance calculation. This presentation is intended to provide an overview of the process.

## Slide 5: Other PSCI PiE Presentations and Reference Files
5- part webinar series on PiE, AMR, and best effluent managing practices
Part 1 - Managing APIs in manufacturing effluent
Part 2 - Managing APIs in manufacturing effluent
Part 3 - Managing APIs in manufacturing effluent
Part 4 - Managing APIs in manufacturing effluent
Part 5 - Antimicrobial resistance
AMR Industry Alliance – Best Practices for Managing Antibiotic Waste
Link
Guidance for Calculating Dilution Factors considering Mixing Zones
Link
PSCI PEC:PNEC Calculator Tool
Link

## Slide 6: Goal of this Presentation
Provide an overview of the mass balance approach for estimating API losses from manufacturing to determine the Predicted Environmental Concentration (PEC) and Risk Quotient (RQ).
The following documents will be available on the PSCI website.
This presentation (with audio recording)
Mass balance process decision tree / flow chart
Detailed guidance presentation for different types of manufacturing: OSD, Sterile, API Chemical Synthesis
Example calculations and reporting template
Example Section of Detailed Guidance Flowchart

## Slide 7: Terminology and Acronyms
eMax – Estimated maximum mass of API discharged to the environment during a 24-hour period. The goal of this guidance is to calculate and refine the eMax value.
PEC – Predicted Environmental Concentration of an API in the receiving water body (µg/L).
PNEC – Predicted No Effect Concentration of an API (µg/L).
Several values – chronic environmental toxicity is normally the lowest.
RQ – Ratio of PEC/PNEC. If RQ >=1, indicates there is risk associated with the discharge of API.

## Slide 8: Mass Balance Process Overview – Background Information
The detailed guidance contains 8 steps. Steps increase in complexity as you go.
Step 1: Select the product and specific SKU for
evaluation.
Step 2: Determine if API Losses can be discharged to the environment.
If possible, continue with assessment.
If not possible, skip to documentation.
Step 3: Obtain PNEC and River Flow Information
Select values based on company and/or PSCI guidance.
Not necessary to perform mass balance – optional step.

## Slide 9: Mass Balance Process Overview – Background Information
The detailed guidance contains 8 steps. Steps increase in complexity as you go.
Step 1: Select the product and specific SKU for
evaluation.
Step 2: Determine if API Losses can be discharged to the environment.
If possible, continue with assessment.
If not possible, skip to documentation.
Step 3: Obtain PNEC and River Flow Information
Select values based on company and/or PSCI guidance.
Not necessary to perform mass balance – optional step.

## Slide 10: Mass Balance Process Overview – Background Information
The detailed guidance contains 8 steps. Steps increase in complexity as you go.
Step 1: Select the product and specific SKU for
evaluation.
Step 2: Determine if API Losses can be discharged to the environment.
If possible, continue with assessment.
If not possible, skip to documentation.
Step 3: Obtain PNEC and River Flow Information
Select values based on company and/or PSCI guidance.
Not necessary to perform mass balance.

## Slide 11: Mass Balance Process Overview – Conservative Assessment
Step 4a: Obtain batch record information for selected product.
Step 4b: Use batch record information to calculate eMax.
Assume all losses go to wastewater.
Conservative, easy to calculate.
Step 4c: Calculate PEC/PNEC (RQ) value using eMax.
If RQ < 1, skip to documentation.
If RQ > 1, proceed to Step 5 to refine mass loss estimate.

## Slide 12: Mass Balance Process Overview – Conservative Assessment
Step 4a: Obtain batch record information for selected product.
Step 4b: Use batch record information to calculate eMax.
Assume all losses go to wastewater.
Conservative, easy to calculate.
Step 4c: Calculate PEC/PNEC (RQ) value using eMax.
If RQ < 1, skip to documentation.
If RQ > 1, proceed to Step 5 to refine mass loss estimate.

## Slide 13: Mass Balance Process Overview – Conservative Assessment
Step 4a: Obtain batch record information for selected product.
Step 4b: Use batch record information to calculate eMax.
Assume all losses go to wastewater.
Conservative, easy to calculate.
Step 4c: Calculate PEC/PNEC (RQ) value using eMax.
If RQ < 1, skip to documentation.
If RQ > 1, proceed to Step 5 to refine mass loss estimate.

## Slide 14: Mass Balance Process Overview – Refine Assessment (1/2)
Step 5: Determine other locations where losses occur.
Dust losses
Solvent disposal
Cleaning removal
QA/QC samples
If there are no other loss locations, then document results from Step 4.
Step 6: Develop a block diagram to track losses associated with production.

## Slide 15: Mass Balance Process Overview – Refine Assessment (1/2)
Step 5: Determine other locations where losses occur.
Dust losses
Solvent disposal
Cleaning removal
QA/QC samples
If there are no other loss locations, then document results from Step 4.
Step 6: Develop a block diagram to track losses associated with production.

## Slide 16: Mass Balance Process Overview – Refine Assessment (2/2)
Step 8: Document results and assumptions using standardized template.
Step 7b: Recalculate RQ value using new mass loss estimate.
If RQ > 1 and further refinement is possible, return to step 7a.
Step 7a: Populate block diagram with process loss information.
Dust losses
Solvent disposal
Cleaning removal

## Slide 17: Mass Balance Process Overview – Refine Assessment (2/2)
Step 8: Document results and assumptions using standardized template.
Step 7b: Calculate new eMax, RQ values
If RQ > 1 and further refinement is possible, return to step 7a.
Step 7a: Populate block diagram with process loss information.
Dust losses
Solvent disposal
Cleaning removal

## Slide 18: Mass Balance Process Overview – Refine Assessment (2/2)
Step 8: Document results and assumptions using standardized template.
Step 7b: Calculate new eMax, RQ values
If RQ > 1 and further refinement is possible, return to step 7a.
Step 7a: Populate block diagram with process loss information.
Dust losses
Solvent disposal
Cleaning removal

## Slide 19
To ask questions, please use the ‘Chat’ or ‘Q&A’ function on the right-hand side of your screen

## Slide 20: Step 1: Select a Product for Evaluation
Example of Product Selection:
Choose product with the highest potential eMax
In this case, 500 MG tablet product has highest API/campaign
Factors to consider when selecting a product for evaluation:
Mass of API per batch
Number of batches per campaign
Concurrent manufacturing
Purpose:
1. Select product for evaluation
There may be multiple products made at your facility which contain the same API.
Carefully select the product(s) being assessed so PEC estimate will be conservative.

## Slide 21: Step 2: Determine if API Losses are Discharged to the Environment via Wastewater
Purpose:
Determine if the selected product can discharge API to the environment via water.
If yes, proceed with assessment.
If no, PEC value is 0. Document results.
2. Is API discharged from the process to water that ultimately reaches the environment?
What happens to your facility’s liquid waste?
Sent directly to a water body.
Sent to an offsite WWTP, which discharges into a water body
Your Facility
Onsite WW Treatment
Municipal WW Treatment
Receiving Water Body
If your facility’s liquid waste does not go to environment, confirm the following…
No process wastewater discharged onsite or offsite
All API-containing wastewater incinerated or sent to a closed-loop zero-liquid discharge (ZLD) system.
Offsite incineration facilities are licensed and audited.
If wastewater is sent to a closed-loop ZLD system, no residual water discharged or used onsite or offsite.
  Note: this includes water used for irrigation.

## Slide 22: Step 3: Obtain PNEC Information
Purpose:
3. Obtain PNEC and receiving water body information. Enter this information into the PEC:PNEC Calculator Tool.
Gather information necessary to calculate PEC/PNEC ratio.
You may need to determine the Risk Quotient (RQ), which is the ratio of PEC/PNEC.
The PSCI PEC:PNEC Calculator tool is designed to calculate Risk Quotient values automatically.
Input relevant Predicted No Effect Concentration (PNEC) value(s)
PNEC information can come from several sources.
WET Center
AMR Industry Alliance
Original innovator of API
Requester of PEC assessment may provide
Calculator Tool Interface for Entering PNEC Information
If PNEC data is not available, the eMax and PEC can still be determined.

## Slide 23: Step 3: Obtain Water Body Information
Purpose:
3. Obtain PNEC and receiving water body information. Enter this information into the PEC:PNEC Calculator Tool.
Gather water body information necessary to calculate PEC value.
PEC is a measure of the concentration of API in the water body receiving API from manufacturing wastewater. This is typically a river, stream, lake or ocean.
PEC will depend on the type, flow, and size of the dilution/mixing zone in the receiving water body.
Policies for establishing dilution volume vary by company.
For River or stream – typically low flow value used:
10th percentile, 5th Percentile, Q710
Data may be available from local environmental agencies
If detailed flow data not available, fraction of average flow
If water body data is not available, the PEC can still be determined.
Calculator Tool Interface for Entering Water Body Information
For Ocean or Lake:
Dilution volume chronic ≈ 10x average wastewater flow
Dilution volume acute ≈ 2x average wastewater flow
Water body specific mixing zone information

## Slide 24: Step 4: Gather Production Yield Information
First-pass mass loss estimate can be established using yield data, where all losses are assumed to go to wastewater.
Note – this is the theoretical worst-case scenario since it assumes all losses (e.g., dust, cleaning, samples, etc.) from the campaign are sent to wastewater at the end of campaign. Requires little effort, simple approach used to determine if PEC/PNEC > 1 is possible.
Purpose:
4a. Obtain & review production yield information from a recent, representative production campaign
Generate an initial, conservative mass loss estimate (eMax). Use PEC:PNEC Calculator tool to determine if further evaluation is warranted.
Obtain completed batch record for recent, representative production campaign.
“Recent” = Completed within the past 12 months.
“Representative”
  If the product is produced in multi-batch campaigns, use campaign with the highest number of batches.
  If the product is produced in single batch campaigns, use campaign with lowest production yield.

## Slide 25: Step 4: Gather Production Yield Information
First-pass mass loss estimate can be established using yield data, where all losses are assumed to go to wastewater.
Note – this is the theoretical worst-case scenario since it assumes all losses (e.g., dust, cleaning, samples, etc.) from the campaign are sent to wastewater at the end of campaign. Requires little effort, simple approach used to determine if PEC/PNEC > 1 is possible.
Purpose:
4a. Obtain & review production yield information from a recent, representative production campaign
Generate an initial, conservative mass loss estimate (eMax). Use PEC:PNEC Calculator tool to determine if further evaluation is warranted.
Mass of API per batch * batches/campaign * (1- Production Yield) = Total Losses = eMax

## Slide 26: Step 4: Use eMax to Calculate PEC Value
With eMax, PNECs, and receiving water data, we can calculate an initial RQ (PEC/PNEC) value.
PSCI has released a calculator tool to automate calculation of RQ values.
Purpose:
4a. Obtain & review production yield information from a recent, representative production campaign
Generate an initial, conservative mass loss estimate (eMax). Use PSCI PEC:PNEC Calculator tool to determine if further evaluation is warranted.
Because at least one RQ value is greater than 1, we will refine the assessment further.
This will be done by accounting for known losses.

## Slide 27: Step 5: Compile List of API Loss Locations
Create a list of locations where API is lost during production and cleaning.
Wastewater
Dust collection
Solvent streams
Cleaning material sent to hazardous waste (rags, mops, etc.)
Reject and samples sent to hazardous waste
This will require the input of process experts from your facility.
Purpose:
Check if API losses can be sent to locations other than wastewater.
5. Can API losses be sent to locations other than wastewater?

## Slide 28: Step 6: Develop a Process Block Diagram
A block diagram will help you understand and account for losses of material in each step.
We will add numbers to the diagram in the next step.
Production
Yield 2
(e.g., Filling)
Losses to Wastewater
System (D1)
Material Input
Losses to Solid Disposal (C1)
Production
Yield 1
(e.g., Mixing)
Losses to Solid Disposal (C2)
Material Output
API Input (A1)
Excipient Input (B1)
Material Output
API to Product (A3)
Excipient to Product (E3)
API Output (A2)
Excipient Output (B2)
Losses to Wastewater
System (D2)
Purpose:
6. Develop process block diagram to identify losses from manufacturing.
Create a block diagram that shows the production process.

## Slide 29: Step 7: Populate Balance with Known/Estimated Losses
From the batch record, obtain the following data on accountable losses.
Use batch records to update block diagram with accountable loss information.
7a. Estimate other losses. Update block diagram and mass balance.
Purpose:
Total Material into Yield 1
kg excipient/campaign
kg API/campaign
Step 1
Dry Cleaning Mass
Waste/Rejected Mass
Central Dust
Collection Mass
Residual Mass
Washed to Drain
Product Mass
Sample Mass
Never Accounted for
in Batch Records
Sometimes Accounted
for in Batch Records
Always Accounted for
in Batch Records

## Slide 30: Step 7: Populate Balance with Accountable Losses
Production
Yield 2
(Filling)
Losses to Wastewater System
Material Input
Losses to Waste Disposal
Production
Yield 1
(Mixing)
Material to Product
Material Output
Losses to Waste Disposal
7a. Estimate other losses. Update block diagram and mass balance.
Use batch records to update block diagram with accountable loss information.
Losses to Wastewater System
Purpose:

## Slide 31: Step 7: Populate Balance with Accountable Losses
Production
Yield 2
(Filling)
Losses to Wastewater System
Material Input
Losses to Waste Disposal
Production
Yield 1
(Mixing)
300 kg material/campaign
30 kg API/campaign
Material to Product
285.0 kg material/camp.
28.5 kg API/campaign
Material Output
280.0 kg material/camp.
28.0 kg API/campaign
Losses to Waste Disposal
7a. Estimate other losses. Update block diagram and mass balance.
Use batch records to update block diagram with accountable loss information.
Losses to Wastewater System
Purpose:
1. Production Yield
Mass moving from step to step

## Slide 32: Step 7: Populate Balance with Accountable Losses
Production
Yield 2
(Filling)
Losses to Wastewater System
Material Input
Losses to Waste Disposal
Production
Yield 1
(Mixing)
300 kg material/campaign
30 kg API/campaign
Material to Product
285.0 kg material/camp.
28.5 kg API/campaign
Material Output
280.0 kg material/camp.
28.0 kg API/campaign
10.0 kg material/campaign
1.0 kg API/campaign
Losses to Waste Disposal
2.5 kg material/campaign
0.3 kg API/campaign
7a. Estimate other losses. Update block diagram and mass balance.
Use batch records to update block diagram with accountable loss information.
Losses to Wastewater System
Purpose:
1. Production Yield
Mass moving from step to step
2. Accountable Losses
Known losses in each step

## Slide 33: Step 7: Populate Balance with Accountable Losses
Production
Yield 2
(Filling)
Losses to Wastewater System
Material Input
Losses to Waste Disposal
Production
Yield 1
(Mixing)
300 kg material/campaign
30 kg API/campaign
Material to Product
285.0 kg material/camp.
28.5 kg API/campaign
Material Output
280.0 kg material/camp.
28.0 kg API/campaign
Losses to Waste Disposal
2.5 kg material/campaign
0.3 kg API/campaign
7a. Estimate other losses. Update block diagram and mass balance.
Use batch records to update block diagram with accountable loss information.
Losses to Wastewater System
Purpose:
5.0 kg material/campaign
0.5 kg API/campaign
2.5 kg material/campaign
0.3 kg API/campaign
1. Production Yield
Mass moving from step to step
3. Losses to Wastewater
Calculate by difference
2. Accountable Losses
Known losses in each step
10.0 kg material/campaign
1.0 kg API/campaign

## Slide 34: Step 7: Differences for Oral Solid Dose (OSD) Products 1/2
OSD products (such as capsules and tablets) typically have dust losses which are rarely accounted for in batch records.
Overhead dust collection
Dry cleaning equipment – vacuums, rags, etc.
Overview of estimating losses for OSD production.
Purpose:
7a. Estimate other losses. Update block diagram and mass balance.
Estimating overhead dust losses – 3 Methods
Dust collection experiment
Estimate aggregate dust factor using waste records.
If 1 and 2 are not possible, estimate removal percentage.
Estimating dry cleaning losses
Measure collected material during campaign
Existing cleaning efficiency data
If there is not sufficient data, do not assume API removal via cleaning.

## Slide 35: Step 7: Differences for Oral Solid Dose (OSD) Products 2/2
Loss calculation for OSD should be done on a per campaign basis.
Track accumulating losses from batch to batch during a campaign.
When estimating losses from OSD production, consider cleaning schedule.
Minor cleaning between batches – typically minor dry cleaning
Final major clean with water will contain accumulated losses from several batches.
If your minor cleaning procedure significantly reduce the losses in the production room, it may be possible to perform calculation on a per batch basis.
Rinses of production equipment
Vacuuming of equipment and surrounding room
Effects of multi-batch campaign production for OSD products.
Purpose:
7a. Estimate other losses. Update block diagram and mass balance.

## Slide 36: Step 7: Differences for Oral Solid Dose (OSD) Products
Production
Yield 2
(Encapsulation)
Losses to Wastewater System (D1)
Material Input
Losses to Waste Disposal (C1)
Production
Yield 1
(Granulation)
Material to Product
Material Output
Losses to Waste Disposal (C2)
Losses to Wastewater System (D2)
Losses to Dust Collection System
Losses to Dust Collection System
Effects of multi-batch campaign production for OSD products.
Purpose:
7a. Estimate other losses. Update block diagram and mass balance.

## Slide 37: Step 7: Differences for Oral Solid Dose (OSD) Products
Production
Yield 2
(Encapsulation)
Losses to Wastewater System (D1)
Material Input
Losses to Waste Disposal (C1)
Production
Yield 1
(Granulation)
200.0 kg API/batch
600.0 kg API/campaign
Material to Product
180.0 kg API/batch
540.0 kg API/campaign
Material Output
175.0 kg API/batch
525.0 kg API/campaign
Losses to Waste Disposal (C2)
Losses to Wastewater System (D2)
Losses to Dust Collection System
Losses to Dust Collection System
1. Production Yield
Mass moving from step to step
Effects of multi-batch campaign production for OSD products.
Purpose:
7a. Estimate other losses. Update block diagram and mass balance.

## Slide 38: Step 7: Differences for Oral Solid Dose (OSD) Products
Production
Yield 2
(Encapsulation)
Losses to Wastewater System (D1)
Material Input
Losses to Waste Disposal (C1)
Production
Yield 1
(Granulation)
200.0 kg API/batch
600.0 kg API/campaign
Material to Product
180.0 kg API/batch
540.0 kg API/campaign
Material Output
175.0 kg API/batch
525.0 kg API/campaign
Losses to Waste Disposal (C2)
Losses to Wastewater System (D2)
Losses to Dust Collection System
Losses to Dust Collection System
1. Production Yield
Mass moving from step to step
2. Accountable Losses
Known losses in each step
2.0 kg API/batch
6.0 kg API/campaign
1.0 kg API/batch
3.0 kg API/campaign
Effects of multi-batch campaign production for OSD products.
Purpose:
7a. Estimate other losses. Update block diagram and mass balance.

## Slide 39: Step 7: Differences for Oral Solid Dose (OSD) Products
Production
Yield 2
(Encapsulation)
Losses to Wastewater System (D1)
Material Input
Losses to Waste Disposal (C1)
Production
Yield 1
(Granulation)
200.0 kg API/batch
600.0 kg API/campaign
Material to Product
180.0 kg API/batch
540.0 kg API/campaign
Material Output
175.0 kg API/batch
525.0 kg API/campaign
9.0 kg API/batch
27.0 kg API/campaign
Losses to Waste Disposal (C2)
Losses to Wastewater System (D2)
Losses to Dust Collection System
Losses to Dust Collection System
1.5 kg API/batch
4.5 kg API/campaign
1. Production Yield
Mass moving from step to step
2. Accountable Losses
Known losses in each step
3. Dust Losses
Estimate via 1 of 3 methods
2.0 kg API/batch
6.0 kg API/campaign
1.0 kg API/batch
3.0 kg API/campaign
Effects of multi-batch campaign production for OSD products.
Purpose:
7a. Estimate other losses. Update block diagram and mass balance.

## Slide 40: Step 7: Differences for Oral Solid Dose (OSD) Products
Production
Yield 2
(Encapsulation)
Losses to Wastewater System (D1)
Material Input
Losses to Waste Disposal (C1)
Production
Yield 1
(Granulation)
200.0 kg API/batch
600.0 kg API/campaign
Material to Product
180.0 kg API/batch
540.0 kg API/campaign
Material Output
175.0 kg API/batch
525.0 kg API/campaign
9.0 kg API/batch
27.0 kg API/campaign
Losses to Waste Disposal (C2)
3.0 kg API/batch
9.0 kg API/campaign
Losses to Wastewater System (D2)
10.0 kg API/batch
30.0 kg API/campaign
Losses to Dust Collection System
Losses to Dust Collection System
1.5 kg API/batch
4.5 kg API/campaign
1. Production Yield
Mass moving from step to step
2. Accountable Losses
Known losses in each step
3. Dust Losses
Estimate via 1 of 3 methods
4. Cleaning Information
Via dry cleaning experiment
Effects of multi-batch campaign production for OSD products.
Purpose:
7a. Estimate other losses. Update block diagram and mass balance.

## Slide 41: Step 7: Differences for Oral Solid Dose (OSD) Products
Production
Yield 2
(Encapsulation)
Losses to Wastewater System (D1)
Material Input
Losses to Waste Disposal (C1)
Production
Yield 1
(Granulation)
200.0 kg API/batch
600.0 kg API/campaign
Material to Product
180.0 kg API/batch
540.0 kg API/campaign
Material Output
175.0 kg API/batch
525.0 kg API/campaign
9.0 kg API/batch
27.0 kg API/campaign
Losses to Waste Disposal (C2)
3.0 kg API/batch
9.0 kg API/campaign
Losses to Wastewater System (D2)
10.0 kg API/batch
30.0 kg API/campaign
Losses to Dust Collection System
Losses to Dust Collection System
1.5 kg API/batch
4.5 kg API/campaign
1. Production Yield
Mass moving from step to step
2. Accountable Losses
Known losses in each step
3. Dust Losses
Estimate via 1 of 3 methods
4. Cleaning Information
Via dry cleaning experiment
5. Losses to Wastewater
Calculate by difference
Effects of multi-batch campaign production for OSD products.
Purpose:
7a. Estimate other losses. Update block diagram and mass balance.
1.0 kg API/batch
3.0 kg API/campaign
0.5 kg API/batch
1.5 kg API/campaign

## Slide 42: Step 7: Recalculate PEC/PNEC Ratio
Return to calculator tool with new eMax value.
Updated RQ (PEC/PNEC) ratio is < 1. No further refinement is required.
Proceed to Step 8 to document results and assumptions.
Purpose:
Calculate PEC/PNEC ratio using PSCI calculator tool.
7b. Recalculate RQ value using refined mass loss estimate.

## Slide 43: Step 8: Document Results, Assumptions, and Supporting Data
Steps to Complete Documentation:
Save assessment files in a single location. Make sure to include…
  PNEC values for the selected API (as well as their source)
  Data used to calculate receiving water body dilution volume.
  Mass balance calculation
  Batch record information
  Documentation to justify loss values to dust, cleaning, etc.
Complete the “Documentation” tab of the “PSCI Example Calculation” Excel file.
Purpose:
8. Document results, assumptions, and supporting data.
Record the results of the PEC assessment, along with the assumptions and supporting data.

## Slide 44
To ask questions, please use the ‘Chat’ or ‘Q&A’ function on the right-hand side of your screen